pwd
ls
ll
cd
mkdir
mv
cp
rm
tree  show tree
readlink -f  search for filepath
du -h -c --max-depth 1 /home/*  disk usage im home verzeichnis (Speicherverbrauch)
wc (word count)
grep (word selection, complicated read man)
curl
echo
sed ‘1d’  remove first line
cut -d  cut everything out except (specify with tabnumber like: f1,3), -d for delimiter
sort
uniq  uniq -c = count
|  pipe output from before = input for next command
ln : link directories
/proc/cpuinfo  Path zur Cpuinfo
history
sudo
jupyter lab
anaconda-navigator
ls ../../../[abx]*sh → alles was mit a, b od x beginnt und mit sh aufhört
less /../. → looking at file contents
head /../../. → first 10 lines of a file
head -20  first 20 lines of a file etc. (head -30 = first 30)
tail =//= → last 10 lines of a file
nano  simple text editor (e.g. nano /home/mathias/blabla.txt )
man → manual
help → similar
file → determine file type
lsblk → inspect block devices
which 'command'→ directorie of the command
type → info about command type
whatis → manual page short
cut → print selected parts of lines
e.g. | cut -d; -f2 | → print the second column of a semicolon (;) separated/delimited file
sort → sortieren ( sort -n → sort numerically)
uniq → alle einzelnen
apt → interacting with the Debian package manager apt
dpkg  package manager
aptitude  interface for apt package manager
&& → second command only if first was succesful
|| → second command only if first wasnt succesful
# to make a comment
Ctrl+C – Interrupt currently running process
Ctrl+Z – Suspend currently running process
Ctrl+D – Logout e.g. from the shell or the Python interpreter (sends an EOF ("end of file") character, signifies end of input)
Text processing shortcuts:
Ctrl+A – Jump to beginning of line
Ctrl+E – Jump to end of line
Ctrl+L – Clear screen (same as clear)
Shift+↑/↓ or PageUp/PageDown – Scroll in the terminal
Ctrl+U – Delete to the beginning of line (undo?)
Ctrl+K – Delete to the end of line (kill?)
Ctrl+W – Delete word left of cursor
Alt+B/F – Jump one word backward or forward (might be setup-dependent); also try Alt+←/→
Ctrl+Y – Retrieve (yank) last item that was deleted or cut
top → system monitor
htop → system monitor advanced
env
printenv
find
echo $((2 + 2))  calculator
echo {1..10}  brace expansion
Jobs:
kill
killall
pidof
pgrep
ps  processes
jobs
> = redirect to file
>> = append to file (inspect with tail)
| = connect stdout to stdin of another process
< = redirect stdin eg. read from file
/dev/null  discard input

https://www.cyberciti.biz/faq/linux-unix-bsd-extract-targz-file/  tar commands simply (for bash)
tar -zxvf  unpack archive

ls -1 | wc -l  count how many files in working directory (1. Ls with one line per file, 2. Count lines)

grep -r TGAAAAGTG ./  searches all files in the current directory that have this pattern (TGAAAAGTG)

grep -c “^>” ./filename  counts how many lines start with >, ^this symbolizes the start of the line

With awk, we can process text files. Awk assigns some variables for each data field found:
$0 for the whole line
$1 for the first field
$2 for the second field
$n for the nth field.
‘{print $1}’ prints the first field before a whitespace.
# The whitespace character like space or tab is the default separator between fields in awk.
grep -v “>” file.fasta > file_headers_removed.fasta or sed ‘/^>/d’ file.fasta > file_headers_removed.fasta
-v is --invert match, this would delete all lines that have a > (for sed all lines starting with >)
grep -v “^$”  deletes all blank lines (also awk NF, sed ‘/^$/d’)
^ this stands for the start of the line and this $ stands for the end of the line, the d in sed deletes the lines with the corresponding pattern
grep “^>” file.fasta | awk ‘{print$1}’  this would take only the lines with > and take only the first field, so for a fasta file only the sequence ID

chmod +x  make a script runnable

-d /pathtodirectory  check if a directory exists
-e /pathandfile  test if a file exists